## Slide 1: electric fleet: three points of view
Gretha van Velthuizen (manager logistics) & Janine van Verseveld (contract manager)

## Slide 2: Point of view: 1. Network design 2. Planning 3. perations

## Slide 3: Keolis Netherlands ZE fleet
Provincie Utrecht
7 BYDs
Almere
7 BYDs
IJssel-Vecht
259 BYDs

## Slide 4: 1. Network design
Important starting point for transportation choices with electric buses:
Our passengers should not be affected by planning. No matter the choice of buses.
    Lower range -> more buses + shorter circulations
    Choice to increase frequency on lines where larger vehicles previously ran
    Build departure time at the most ideal moment and no longer at the same time the other bus arrives
    We have built more ‘space’ into the circulations.
3 disciplines, 3 points of view

## Slide 5: 1. Network design
An electric fleet also has a few drawbacks for passengers:
Interconnected lines: mainly city services
Optimal layout of bus station is a big advantage for passengers
3 disciplines, 3 points of view

## Slide 6: 2. Planning
State of charge ‘SOC’
The state of charge is a percentage display of the current capacity compared to the maximum battery capacity.
3 disciplines, 3 points of view
SOC + VEHICLE RUNS + ROUTERESTRICTIONS = PRIORITY #1

## Slide 7: 2. Planning
Order of construction:
1. Timetable (schedule)
2. Loading plan + vehicles runs
3. Drivers’ services
3 disciplines, 3 angles
Balance between more charging points with fast charging vs. efficiency
Less fast charging needed with broken circuits
Less trips to the garage due to fast charging at drop-off points
Fast charging can save on number of vehicles
Smaller vehicles often cannot be charged quickly
Pantograph charging is vulnerable within the transport system (up and down = fragile and charging time)
Opportunity charging = minimum charging time of 10 minutes

## Slide 8: From timetable to.....simple example of concept!

## Slide 9: …….vehicle runs
C2 is driven exclusively with one kind of vehicle (13m). The blue blocks are loading moments, in this case on the buffer in Apeldoorn, so loading under the pantograph.

## Slide 10: 2. Planning
Consequences of planning with ZE buses:
More bus changes in services
Opportunity charging and overnight charging dependent on planning structure
Planning tight schedule is risky in case of delays, breakdowns and failures
Different bus types cannot always be switched (combi loading and bus)
Technical planning software under development
3 disciplines, 3 points of view

## Slide 11: 3. Logistics and operations
Different approach in the operation by:
    Load and depot management system
      Monitoring by LMS of electricity dosage to buses (maximum capacity network connection)
      Huge dependency on charging infrastructure
      Fragmented charging per hour block and right match of bus and charging station
    Control center
      Different approach on coordination in operations
      Tight control on SOC vs circulation, recharging and relationship with weather / driver’s influence
    Logistics planner is crucial in relation to availability of buses / maintenance
    Allocate buses via system to drivers
      Park buses at the right charging station
      Distribution of buses via charging plan
3 disciplines, 3 points of view

## Slide 12: What about the opinion of our passengers?

## Slide 13
Provincie Utrecht

## Slide 14
IJssel-Vecht

## Slide 15: Conversation and questions?
PASSENGERS - ELECTIC BUSES - NETWORK DESIGN:
WHAT OPPORTUNITIES AND THREATS DO YOU SEE IN THE NEAR FUTURE?