## Slide 1: Driver and Staff Training in e-bus Deployment in Turku
Rami Wahlsten
eBussed Good Pactice event 31.3.2022 Utrecht
eBussed

## Slide 2: Contents
Video
General Facts
Driver Training
  Basic operation
  Practical Training
  Economical driving
Service Crew Training
  Bus and Charger Safety
Rescue and Towing Staff Training
Conclusions
eBussed
eBussed

## Slide 3: Short video about the Good Practice
https://youtu.be/5XeRSAMSqCY

## Slide 4: General Facts

## Slide 5: E-bus Pilot Info and Bus Specifications
E-Bus pilot
Single bus line electrified in 2016
System consists of 6 e-buses,
  2 opportunity chargers,
  6 depot chargers
Linkker 13LE Electric Specifications
Length 12.8 m
Aluminium body, 10 100 kg
Passenger capacity 36 + 42 = 80
Permanent magnet motor 180 kW
eBussed

## Slide 6: Linkker 13LE Electric Battery and Recharging
LTO battery 55 kWh
  Recharging power 300 kW
  Driving range 35 ‒ 50 km
Opportunity Charging
  Inverted pantograph
  Both ends of line (12.5 km)
  3 ‒ 5 min
Depot charging
  22 kW / 50 kW
High voltage also used for
  Heat pump (15 kW / 15 kW)
  Air Compressor
  Power Steering
  DC / DC (for 24 V)
Source: www.linkkerbus.com
eBussed

## Slide 7: Objectives of Staff Training Facts Included in Training
Benefits of the electric bus
Familiarity with Linkker technology
Operating and driving the eBus
Charging the eBus
Safety issues
Solving problems

## Slide 8: Driver Training

## Slide 9
We started preparing for training by visiting the bus factory.
Visits started early: at the first time only the chassis of the first bus was ready.
We got training material, which
  we modified for our use
We had also the opportunity to test drive the bus before it was registered.
Driving motor
Driver Training Basic Operation

## Slide 10: Driver Training Basic Operation
Air compressor
Power steering, inverter and DC / DC converter
Heating and air-conditioning
Location of switches and warning lights etc. in the instrument cluster
Location of high-voltage components
Location of high-voltage wiring
Operation of heating and air-conditioning

## Slide 11: Driver Training Practical Training
Getting to know the bus generally
How to drive the bus
How to charge the bus (both pantograph and cable charging)
Problem solving
eBussed

## Slide 12: Driver Training Economical Driving
Was organized after 6 months of operation
Target group: about 100 drivers
Morning part: theoretical training
Afternoon: driving under super-vision of the trainer
Issues discussed:
  Moderate speed (max 40 km/h)
  Rapid accelerations
  Mild and early decelerations
  Anticipation: avoiding braking, maintaining the speed gained
eBussed
eBussed

## Slide 13
STOP
STOP
Start and finish
3 laps (3 x 1.8 km = 5.4 km)
Stop of 30 sec at each Bus Stop
Total of 16 stops
BUS LINE SIMULATION IN A RESTRICTED AREA WITH NO INTERFERING TRAFFIC
Comparison of electricity consumption using different driving styles
Driver Training Preparation for Eco-training

## Slide 14
Chart: Max speed 35 km/h, 15.6 min
Chart: Max speed 45 km/h, 13.3 min
35 km/h
45 km/h
ΔSOC 5.5 %
ΔSOC 7.0 %
Consumption
reduction
21 %
Driver Training Preparation for Eco-training

## Slide 15: Service Crew Training

## Slide 16: Service Crew Training Bus and Charger Safety
Emergency stop switches
High voltage powerlines
Resetting the system after accident

## Slide 17: Rescue and Towing Staff Training

## Slide 18
How to lead the passengers out
Disconnecting the high-voltage battery
Locations of high-voltage components and wiring
Locations of the 24 V main switches
Preconditioning the vehicle for towing
Use of the towing hitch
Rescue and Towing Staff Training Abnormal Situations

## Slide 19: Conclusions

## Slide 20: Linkker 13LE Electric Bus Conclusions
The bus is energy-efficient, battery-to-wheel (~1 kWh/km)
  Grid-to-wheel consumption 15% higher than battery-to-wheel
Smooth ride (no gear changes)
Low noise level
Problems existed with the diesel powered interior heater
Diesel powered heater was replaced by an electric heater => OK
System realiability (bus and re-charging devices) below expectations
eBussed

## Slide 21: Thank you!
eBussed