## Slide 1: Good Practice in E-Mobility
Structured approach to e-bus transition at VHH Hamburg

## Slide 2: The Transition to E-Mobility
is a marathon, not a sprint (for VHH approx. 10-14 years to all electric)
effects almost everyone in the company
brings new complexities to the business
for VHH is an organisational change project
Each company should use workshops to develop their own roadmap to transition.

## Slide 3: 01 - Energy demand of e-bus operations
How to find out how much energy your busses will need?
Estimate energy use per km (e.g. 1,7 kWh/km solo bus / 2,2 kWh/km articulated bus).
Ask the e-bus provider, or even test their buses for this.
Apply to your runs, then draw up needed charging on a timeline.
Add up for a potential load demand curve.

## Slide 4: 02 - Emergency concepts
What emergencies need to be accounted for?
  Loss of power
  Fires or floods etc.
    Design infrastructure with these szenarios in mind (e.g. use redundancies, Investigate own supply renewable energies maybe, find measures to reduce damage, talk with similar services for emergency support plans, have communication strategies in place.
  Plans to provide Emergency services
    E.g. in case of flooding, VHH is obliged to evacuate a certain area along a dike area. What number of buses have to always be ready at short notice? How to we ensure this at all times?
Utrecht Good Practice!

## Slide 5: 03 Battery and charging technology
Make a market analysis to ensure you are not investing in the wrong things.
You can also compare with hydrogyn.

## Slide 6: 04 - charging and battery concepts
Suitability of overnight plug in charging or opportunity charging is largely dependent on parameters such as the traffic network, topography or possibly even climate.

## Slide 7: 05 Processes in depots and workshops
Run through your daily operations but swap in the e-bus as the protagonist.
- What extra information is needed?
- What complications are expected?
- Where does the regular process need to be adapted to suit an e-bus?

## Slide 8: 06 Energy provision
Is enough energy available through the public grid?
Will this be the case in 10 years time when everyone in the neighbourhood has e-cars too?
Collaboration with the grid provider and the energy department of the university of armed forces.
It‘s a strategic matter for cities to have a good understanding of the future needs.
Beware: if there is not enough energy, connecting more can take in some cases several years.

## Slide 9: 07 structural (physical) infrastructure
You will need electrical expertise...
VHH hired new staff and created an entire new department for infrastructure.

## Slide 10: 08 Third-party concepts for energy and infrastructure
Someone else builds your charging infrastructure and you pay an increased price for energy.
Especially suitable for cities where there is a publically owned energy provider (e.g. Darmstadt in Germany).
Alternatively suitable if the charging infrastructure could be beneficially used during the day by another company (carriers, taxies etc.).
This makes a lot of sense for smaller companies too who can not afford to invest in extra staff with electrical expertise to build, run and maintain the infrastructure.
(This was not persued any further by VHH).

## Slide 11: 09 New vehicle scheduling
VHH decided to invest in a new software since the old one was now more than 10 years old and not fit for purpose anymore.
Length of km per run

## Slide 12: 10 Cooperation and strategic partners
VHH naturally cooperated with the Hamburg Hochbahn (the second local public transport provider)
Networking across a platform of public transport providers
Testing ebuses during development stage for a large German manufacturer
Public-public partnership with the Stromnetz Hamburg to use the back-end software that also powers all public car charging points.
Join an EU interreg project!

## Slide 13: 11 Staff training
See good practice from Turku!
Additionally VHH developed a website/app where small information text items can be posted. A great way to keep the drivers updated on project news.

## Slide 14: 12 Financial resources required
Application for federal grants
Loans from the European Investment Bank
Clever accounting?!?

## Slide 15: 13 Vehicle procurement
Number of vehicles and number of charging infrastructure must increase simultaneously.

## Slide 16: 14 Need for development in IT infrastructure
New software at VHH:
Planning SW
Deployment SW
Workshop ticketing
Loadmanagement
Energy Procurement
Amended System:
- ITCS with extra %SOC capabilities

## Slide 17: 15 Planning of infrastructure modification and construction works
Found to be redundant – already part of 07 Infrastructure…

## Slide 18: 16 Traffic concept 2030
Are you expecting to have the exact same service in the future?
Hamburg will be implementing a couple of high density traffic lines (S-Bahn, U-Bahn) which will lead to a change in service requirements for busses.
Generally the city is likely to gain people and therefore the demand in service will increase.
Maybe political vision will change and new mobility solutions implemented. How might this influence your plans?
(… and then there was a pandemic….)

## Slide 19: Plus: Respect the project processes
Make your stakeholder analysis
Identify your risks
Clearly define responsibilities, accountabilities and decision making
Report regularly and frequently (e.g. monthly)
Set yourself some milestones performance indicators to keep on track
Plan to review in certain intervals if your goals are still valid or if you need to make adjustments (things change during such a long project!)
Try to account for the extra efforts needed to accomodate all this.

## Slide 20: Thank you for listening!
Any questions?